## Slide 1
Prof.(Dr.) Rabindranath Bera (Professor, IIIT, KALYANI)
E-mail: rbera@iiitkalyani.ac.in; Mobile : 9475513358
Course Title: 5G and Wireless Technology
Course Code : ECE829
CLASS 17,18,19
Dated 24 March 2025
Mobile Fading Channels
MODULE 1 of the Syllabus:-

## Slide 2: Outline of Presentation
Radio wave Propagation
Time spreading
Doppler Spreading
Fading Channel Summary

## Slide 3: Free Space Propagation
Top
12.1
Only attenuation and AWGN present in the channel:
d
Transmitter
Receiver
No objects present
No reflections
No power absorption by the medium
Power attenuation due to
distance, inverse square law:
  
Ld =  4--------d- 2

## Slide 4
Top
Mobile Fading Channels
Ver 09.725
Notes:
The free space model assumes the following:
The space between antennas is free of objects that might reflect or absorb the radio signal
The atmosphere is a uniform and non absorbing medium
The antenna heights is infinite, therefore the earth is infinitely away from the propagating signal; equivalently the reflection coefficient can be assumed negligible.
Under these conditions, the radio frequency power is attenuated according to an inverse-square law, for an isotropic antenna this attenuation is
Ld =  4--------d- 2
  
where d is the distance between antennas and  is the carrier frequency wavelength. Under the free space assumption, the received power can be easily calculated.

## Slide 5: Multipath Propagation, Fading
Top
12.2
A more realistic propagation scenario: multipath fading:
transmitter
receiver

## Slide 6: Multipath Fading
Top
12.3
Fading: fluctuation in the received signal power due to:
  variations in the received signal amplitude:
variations in the received signal angle of arrival:
A1
A2
A2  A1
variations in the received signal phase:
1

2
1  2
1
2
1  2

## Slide 7
Top
Notes:
Mobile Fading Channels
Ver 09.725
The presence of objects on the radio signal path produces attenuation of its power as they can scatter or absorb part of the signal power, thus producing a variation of the amplitude.
Paths travelling different distances may arrive at the receiver with different phases as well as angle of arrival.

## Slide 8: Large Scale & Small Scale Fading
Top
12.4
Large scale fading: average signal power attenuation or path loss due to motion over large areas;
Small scale fading: large variations of the signal amplitude due to small changes in the distance between transmitter and receiver (also called Rayleigh fading if there is no direct line of sight (LOS) between transmitter and receiver):
antenna position
signal power (dB)
large scale fading
small scale fading

## Slide 9
Top
Notes:
Mobile Fading Channels
Ver 09.725
Large scale fading is due to movement of the transmitter or the receiver (or both) over large areas. The path between them is shadowed by prominent terrain contours such as hills or forests. This kind of fading is characterised by a mean path loss and a log-normally distributed variation about the mean. An estimate of the path loss as a function of the distance can be calculated using these statistics.
Small scale fading is due to small changes in distance (half wavelength) between transmitter and receiver. If the number of paths is large enough and there is no direct line of sight (LOS) between transmitter and receiver the envelope of the received signal can be statistically characterised by a Rayleigh pdf, thus this fading is also called Rayleigh fading. In case there is a direct LOS propagation path, the statistical distribution of the received envelope is Rician.

## Slide 10: Rayleigh Fading Mechanisms
Top
12.5
Rayleigh fading manifests itself in two mechanisms:
  Time spreading introduced by the channel due to multipath (time dispersion);
  Time-variant behaviour of the channel due to motion and changes in the propagation paths.
Rayleigh PDF:
SystemView
0
0
1
1
2
2
3
3
4
4
4.e+3
3.5e+3
3.e+3
2.5e+3
2.e+3
1.5e+3
1.e+3
500
0
Bin Count
Amplitude

## Slide 11: Time spreading
Top
12.6
Multiple paths in the channel: signal arrives at the receiver delayed and attenuated:
1 P
1
P2
P3
2
3
h(t)
time
1 2 3
impulse response
single signal is spread in time due to multipath
channel frequency response
ht = Hf
freq
|H(f)|2
different frequencies suffer different attenuations
finger 1
finger 2
finger 3

## Slide 12: Time variant behaviour of the channel
Top
12.10
Relative movement between transmitter and receiver or of bodies between them produces a spreading of the transmitted signal frequencies: Doppler effect:
1 P
1
P2
P3
2
3
time
1 2 3
impulse response
finger 1
finger 2
finger 3
˜1 ˜
P1
P˜
˜3 P˜ 3
time
˜1 ˜3 ˜2
impulse response
finger 1
finger 2
˜2
2
finger 3
vm
v'm
vm
v'm
ht
h˜ t

## Slide 13
Top
Notes:
Mobile Fading Channels
Ver 09.725
The time variance of the channel is an important factor to take into account when designing a mobile communication system. Fast variations in the channel can cause severe pulse distortion and loss of SNR which can lead to irreducible BER.
Distorted pulses can cause synchronization problems, yielding to PLL failure, as well as problems tracking channel variations by equalizers, which will have to be re-trained more often in order to cope with the channel changing rate.

## Slide 14: Doppler effect
Top
12.11
vm
d
0
dt
c
c
d0 – vmt vmt
c
t = --------- = -------------------- = 0 – --------
c
c
c
vmt 
c d
+ f t – 
cos2f t – t = cos 2f t – 0 + -------- 
= cos 2f
When transmitter and receiver are in relative motion the received carrier frequency is shifted relative to the transmitted carrier frequency;
Doppler effect: single path case:
propagation time, function of time:
transmitted signal: cos 2fct
received signal:
c 0
d
v
m
c
------
f
c
Doppler frequency shift f =
phase term  = 2f 
c speed of light
fc carrier frequency

## Slide 15
Top
Notes:
Mobile Fading Channels
Ver 09.725
A positive or negative Doppler frequency shift appears depending on whether the transmitter is moving toward or away from the receiver. As an example, a person walking at 3 miles/hr will cause a Doppler shift of 4 Hz when the carrier frequency is 910MHz. For the same person travelling in a car at a speed of 60 miles/hr, the Doppler shift introduced will be of 80 Hz.

## Slide 16: Doppler spectrum
Top
12.12
Doppler effect: multipath case:
With multipath: we talk about Doppler spectrum and not Doppler shift.
finger 1
finger 2
finger 3
v
m
v'm
v''m
Different paths have different speed components
vm  v'm  v''m
different Doppler shift for each path
vm fd v'm f 'd v''m f ''d
freq.
When transmitting a sinusoid, three shifted sinusoids are received
Yf
Xf
freq.
fc
fc + fd fc + f 'd
fc + f ''d
Doppler spread

## Slide 17
Top
Notes:
Mobile Fading Channels
In a realistic multipath case, when a single sinusoid is transmitted, instead of being subjected to a simple Doppler shift, it is spread in frequency and is received as a spectrum, called Doppler spectrum. This happens when there is relative movement between transmitter and receiver or when there are moving objects in the transmission path as this produces time variant multipath characteristics.
For a Rayleigh channel the classical Doppler spectrum is [17]
2fd
d
Df = -----1------1 – f  f 21  2
d
f  f
where fd = vmfc  c is the maximum Doppler shift
fc – fd fc fc + fd
freq.
Doppler power spectrum
Df
Another Doppler spectrum model used is the flat spectrum model [17], which is flat over a range of frequencies symmetric to the carrier frequency
Df = -----1------ f  fd
2fd
[17]K. Pahlaven, A.H. Levesque. Wireless Information Networks. John Wiley & Sons, 1995.
Ver 09.725

## Slide 18: Time variant channel: coherence time
Top
12.13
Time variant channel produces fading: as terminals move and paths change, power fluctuates at the receiver;
Coherence time T0 : Expected time duration over which the channel’s response is essentially invariant;
Approximate relation between T0 and fd (Doppler spread):
fd
T0  -1---

## Slide 19
Top
Notes:
Mobile Fading Channels
Ver 09.725
The function Rt called the space time correlation function shown below is the autocorrelation function of the channel response to a sinusoid. This function indicates the amount of correlation between the channel response to a sinusoid sent at time t1 and the response to another sinusoid sent at time t2 .
f
c
c d
f + f
c d
f – f
freq.
Doppler power spectrum
Df
Fourier transform
0
t
T0
Rt
Therefore, the width of the main pulse in Rt is T0 or coherence time which is a measure of the period of time over which the channel’s response is invariant.

## Slide 20: Time variance: fast fading
Top
12.14
Fast fading produces:
  baseband pulse distortion
  loss in SNR
  synchronisation problems (failure of PLL)
Fast fading:
T0  Ts Ts : symbol duration
Fading channel changes several times while a symbol is propagating;

## Slide 21
Top
Notes:
Mobile Fading Channels
Ver 09.725
P.A. Bello and B.D. Nelin. “The influence of fading spectrum on the binary error probabilities of incoherent and differentially coherent matched filter receiver”. IRE Trans. Commun. Sys., Vol. C-10, June 1962, pp. 160-68.
When fast fading occurs, the time when the channel behaves in a correlated manner is short compared to the duration of a symbol. Therefore the symbol will be distorted due to the fact that the received signal’s components are not correlated through time.
The fast fading condition:
T0  Ts
can also be expressed as:
W  fd
where W  --1----
Ts
The distortion and loss of SNR produced by fast fading yields an irreducible error rate, that cannot be overcome by increasing Eb  N0 [•].

## Slide 22: Time variance: slow fading
Top
12.15
Slow fading:
T0  Ts Ts : symbol duration
The channel remains invariant through the duration of a transmission symbol;
Slow fading produces:
  Loss in SNR (as with flat fading).

## Slide 23
Top
Notes:
Mobile Fading Channels
Ver 09.725
With slow fading, the duration in which the channel behaves in a correlated manner is long compared to the time duration of a transmission symbol. Therefore, the channel will remain virtually unchanged during the time a symbol is transmitted, which will not suffer any distortion.
Another condition for slow fading is:
W  fd
When low data rate systems like Morse or teletype were in use, channels could often be considered as fast fading. However, when present high data rate systems are used, channels can generally be characterised as slow fading.

## Slide 24: Fading Channel Summary
Top
12.16
fading channel manifestations
large scale fading
motion over large areas
small scale fading
small changes in position
time variance of channel
mean attenuation vs. distance
variations about the mean
flat fading
time spreading of signal
frequency selective fading
fast fading slow fading